FABRICATING MACHINERY, INC.

6315 TORONTO STREET     DALLAS, TEXAS 75212-3025

(214) 688-0472    FAX (214) 905-9020   sales@fabmachine.com

Quotation Number:

One (1) Used DiAcro Manual Turret Punch

Model:									18

Serial Number:								BE-2115			Built series from 1966-84, but DiAcro did not keep records!

Specifications:

Punch Stations;								18

Throat;									18"

Capacity:								4 Ton

Mild steel 65,000 psi: 2"24ga, 1-7/16"20 ga, 1-1/16"18ga,

13/16"16 ga, and 11/16"14 ga.

Square 1" 20 gauge

A36 steel 80,000 psi:  2"26ga, 1-3/4"24 ga, 1-1/8"20ga,

7/8"18 ga, 11/16"16 ga, and 17/32"14 ga .

Square 1" 22 gauge

Stainless steel 97,000 psi:  2"28ga, 1-7/16"24 ga, 1-1/8"22ga,

15/16"20 ga, 11/16"18 ga, 9/16"16 ga, 7/16"14 ga .

Square 1" 24 gauge

Normal Punch & Die Arrangement

12 stations 	1/16" – 3/4" (max diagonal)

5 stations   	25/32"- 1-7/16"

1 station 	1-15/32" - 2".

Tooling in Machine

Small holders, round;		1/8", 3/16", 1/4", 5/16", 11/32", 3/8", 13/32",

7/16", 1/2", and 2 holders without tooling

Medium holders, round;        	5/8", 3/4", 15/16", 1", 1 1/8", 1 1/4"

Large holder, square;		1" square

Note: the 3/16" and 1/4" round punches need replacing, but other tooling good.

Features:

Punch turret and die plate rotated together via handwheel

(sprocket and chain links handwheel to punch and die turrets).

DiAcro rapid gauging: back and side gauge dials in .001" increments

(does not keep track of tenths, but 100 increments per rotation).

Layout table (factory)

Mounted on 48" square heavy duty steel table.

(2" square tube frame and 1/4" steel table top, see picture)

Price Used as above

F.O.B. FMI-Dallas							$  3,250.00

METAL FABRICATING MACHINE SPECIALIST

New and Used    Sales and Service   Lease Plans Available

Email:sales@fabmachine.com

TERMS AND CONDITIONS OF SALE

1. Machine(s) may or may not conforms to OSHA standards.  It is the responsibility of the purchaser to be sure the machine(s) are in safe operating condition and in compliance with all appropriate OSHA standards before putting the machine(s) into service.

2. Machine usage:

Buyer acknowledges that the goods covered by this quotation were neither designed nor manufactured by seller.  As seller does not know of the specific application of the equipment by buyer, buyer acknowledges that it is the buyer's responsibility to provide proper safety devices for the particular application or use intended by buyer, so as to protect the operator and others from harm, and to comply with all federal, state and local government laws, rules and regulations relating to safety standards and all industry safety standards.

Indemnification:

Buyer hereby (1) waives, releases and discharges any and all claims (with the exception of claims for breach of the agreement), of any and every kind (including but not limited to injury or death of any person or damage to property), which it may have at any time against the Seller, its agents or employees, by reason of or arising out of any condition or defect of the goods sold hereunder, including but not limited to any claimed improper design, specifications or manufacturing defect of goods sold hereunder, or devices; and (2) covenants to indemnify and hold harmless Seller, its agents and employees of, from and against any and all loss, damage, expense, claims, suits, costs of defense, including attorney's fees or liability which Seller or any of its employees may sustain or incur at any time for or by reason of any injury to or death of any person or persons or damage to any property, arising out of any condition or defect or the goods sold hereunder, including but not limited to claimed improper design or manufacturing defect or other defect of the goods sold hereunder, or any claimed inadequate or insufficient safeguards or safety devices, or warnings.

3. Payment:

Used; Full payment prior to shipment.

4. Taxes:

All sales are subject to applicable federal, state, and local use, sales and excise taxes which the buyer agrees to pay, and which may be billed as part of the selling price, or separately, if the Seller is required by any taxing authority to collect and pay such tax.

5. All prices herein quoted are F.O.B. the stated shipping point and are good for a maximum of 30 days unless otherwise stated.  They do not include sales tax.

6. Warranty disclaimer:

Used machine offered  "(s is" loaded on your pick-up or trailer.

Seller makes no warranties of any kind whatsoever, expressed or implied, and ALL IMPLIED WARRANTIES OR MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE HEREBY DISCLAIMED and excluded from this agreement.

All specifications and descriptions of said goods are from catalog or approximation only.

Seller makes no representation or warranty that said goods conform to any specifications, descriptions or condition.  It is the Buyer's responsibility to inspect the goods and to ascertain if the specifications, descriptions and condition of the goods conform to Buyer's requirements.  Full payment prior to shipment.

7. Claims:

Any and all claims for errors in merchandise must be made in writing immediately upon receipt of goods.

No credit will be allowed on returned goods without our prior permission.  It is expressly agreed the Buyer's sole and exclusive remedy for any claims arising under this agreement against Seller shall be limited to return of the goods and repayment of the purchase price, or to repair or replacement of the goods at Seller's option.  In no event shall Seller be responsible for special or consequential damages.