FABRICATING MACHINERY, INC.

6315 TORONTO STREET     DALLAS, TEXAS 75212-3025

(214) 688-0472    FAX (214) 905-9020   sales@fabmachine.com

Quotation number:

One (1) New Tennsmith Hand Brake

Capacities:					HB 121-16	          HB 121-14

Mild steel				16 gauge	         14 gauge

Stainless steel				20 gauge	         18 gauge

Aluminum 6061-T4			.125"		        .150"

Aluminum 6061-T6			.090"		        .105"

Hemming, closed (not mashed)	24 gauge	         22 gauge

Removing angle reduces bending capacity 4 gauges, but hemming not effected.

Bending length				121"		         121"

Maximum lift of beam			2-1/4"		         2-1/4"

Front to rear beam adjusting			½"		         ½"

Minimum reverse bend			¼"		         ¼"

Minimum flange in capacity 			1"		         1"

Dimensions lwh with counterweights		161"x53"x59.5"       162"x54"x63.5"

Weight					            2,875#		         3,250#

Price, f.o.b. TN                       			$6,825.00	         $7,300.00

Special price f.o.b. TN                                    $6,500.00	         $6,950.00

Support leg					$   150.00	         Included

Estimated flat bed tarped partial load             $1,250-$1,500 DFW metroplex

Price f.o.b. FMI-Dallas			$7,250.00                 $7,650.00

Closed hem based upon ½ " minimum flange and just under a thickness gap.

Mashed hem (no gap at all) reduces capacity significantly.

Support leg reduces deflection in bed when head is clamped and will keep

the hem more consistent end to end.

Availability:

METAL FABRICATING MACHINE SPECIALIST

New and Used    Sales and Service   Lease Plans Available

Email:sales@fabmachine.com

TERMS AND CONDITIONS OF SALE

1. Machine(s) may or may not conforms to OSHA standards.  It is the responsibility of the purchaser to be sure the machine(s) are in safe operating condition and in compliance with all appropriate OSHA standards before putting the machine(s) into service.

2. Machine use:

Buyer acknowledges that the goods covered by this quotation were neither designed nor manufactured by seller.  Buyer acknowledges that it is the buyer's responsibility to provide proper safety training for the particular application or use intended by buyer, so as to protect the operator and others from harm, and to comply with all federal, state and local government laws, rules and regulations relating to safety standards and all industry safety standards.

Indemnification:

Buyer hereby (1) waives, releases and discharges any and all claims (with the exception of claims for breach of the agreement), of any and every kind (including but not limited to injury or death of any person or damage to property), which it may have at any time against the Seller, its agents or employees, by reason of or arising out of any condition or defect of the goods sold hereunder, including but not limited to any claimed improper design, specifications or manufacturing defect of goods sold hereunder, or devices; and (2) covenants to indemnify and hold harmless Seller, its agents and employees of, from and against any and all loss, damage, expense, claims, suits, costs of defense, including attorney's fees or liability which Seller or any of its employees may sustain or incur at any time for or by reason of any injury to or death of any person or persons or damage to any property, arising out of any condition or defect or the goods sold hereunder, including but not limited to claimed improper design or manufacturing defect or other defect of the goods sold hereunder, or any claimed inadequate or insufficient safeguards or safety devices, or warnings.

3. Payment Terms:

New; 25% deposit with order, the balance due prior to shipment unless otherwise specified.

Cannot cancel without penalty after manufacturer orders materials or begins manufacturing.

4. Taxes:

All sales are subject to applicable federal, state, and local use, sales and excise taxes which the buyer agrees to pay, and which may be billed as part of the selling price, or separately, if the Seller is required by any taxing authority to collect and pay such tax.

5. All prices herein quoted are F.O.B. McMinnville, TN and are good for a maximum of 30 days unless otherwise stated.  They do not include sales tax.

6. Warranty:

New Goods carry the warranty of the respective original manufacturer.  No other warranty will apply.

Tennsmith machinery and component parts are carefully inspected and tested. Tennsmith agrees that for a period of 12 months from the date of delivery to replace at their option any machine or component thereof proving defective within the above period. Additionally they agree for a period of 36 months to replace component parts proving defective.

All warranty claims are f.o.b. their plant in TN, providing such machine or component is returned freight pre-paid to them. This warranty does not include repair or replacement that is required because of misuse, abuse, or normal wear and tear. Tennsmith is not responsible for cost of repairs attempted outside of their factory without prior authorization.

This warranty is made expressly in place of all other warranties or guarantees, express or implied, with respect to fitness, merchantability, quality, or operability. No claims for defect will be honored if serial number and data tag has been removed or altered.

Accompanying warranty card must be properly filled out within 10 days for warranty coverage.

7. Claims:

Any and all claims for errors in merchandise must be made in writing immediately upon receipt of goods.  No credit will be allowed on returned goods without our prior permission.  It is expressly agreed the Buyer's sole and exclusive remedy for any claims arising under this agreement against Seller shall be limited to return of the goods and repayment of the purchase price, or to repair or replacement of the goods at Seller's option.  In no event shall Seller be responsible for special or consequential damages.